## Slide 2: Impact Analysis
Presented By: Saman Sana
Lecturer
Department of Environmental Sciences
University of Veterinary and Animal Sciences

## Slide 3
Impact Assessment
It refers to the identification and evaluation of environmental changes occurring as a result of implementing a project
What is Impact?
A change in parameters over a specified period within a defined area resulting from a particular activity compared with the situation which would have occurred had the activity not been implemented.
Environmental impact parameters
Notes: Impact analysis - to identify and predict the likely environmental, social and other related effects of the proposal.

## Slide 4
The screening phase of EIA determines whether or not an EIA is required for a particular proposal.
The scoping phase identifies the important issues that should be investigated in detail (making sure that time and money is not wasted investigating issues that are not of concern).
The next stage of the EIA process is when a detailed assessment is undertaken to forecast the characteristics of the main potential impacts. Known as impact analysis, this stage can be broken down into 3 overlapping phases:
Identification
Prediction
Evaluation
3 Phases of Impact Analysis

## Slide 5
Identification: to specify the impacts associated with each phase of the project and the activities undertaken;
Prediction: to forecast the nature, magnitude, extent and duration of the main impacts; and
Evaluation: to determine the significance of the residual impacts i.e. after taking into account how mitigation will reduce a predicated impact.
1)
2)
3)
Tools & Techniques for Impact Identification
  Adhoc method
  Checklist
  Matrices
  Networks
  Overlays and geographic information system (GIS)
  Expert systems
Impact analysis is the technical heart of the EIA process.

## Slide 6: Adhoc Method
Team of experts assembled for a short time to conduct an EIA
Each expert’s conclusions are based on a unique combination of experience, training and intuition
This approach was followed immediately after the enactment of NEPA
Drawbacks:
It may not encompass all the relevant impacts
Criteria used to evaluate impacts are not comparable and can not be replicated

## Slide 7: Checklists
These annotate the environmental features and factors that need to be addressed when identifying the impacts of projects or activities.
These can vary in complexity and purpose, from a simple checklist to a structured methodology or system that also assigns significance by scaling and weighting the impacts
Checklists could be improved and adapted to suit local conditions as experience with their use is gained.
Notes: e.g. Battelle Environmental Evaluation System= This method has been identified as one of the most quantitative methods. In the Battelle method, 78 measurable environmental parameters are divided into four major categories of ecology, environmental contamination, aesthetics, and human interest

## Slide 8
Checklists provide a systematized means of identifying impacts
They also have been developed for application to particular type of projects and categories of impacts (such as dams or road building).
Sectoral checklists often are useful when proponent specialize in one particular area of development.
Disadvantages of checklists:
Ineffective in identifying higher order impacts or inter-relationships between impacts
Types of checklists
  Simple checklist
  Descriptive Checklist
  Scaling Checklist
  Weighting-Scaling Checklist
  Questionnaire Checklist
Notes: It does not illustrate interactions between effects.

## Slide 9
A list of environmental parameters with no guidelines on how they are to be measured and interpreted
Simple checklists
Descriptive checklists
Add to simple checklists as they not only list the aspects to be considered but provide additional background information on each aspect
Scaling checklists
It is similar to a descriptive checklist , but with additional information on subjective scaling of the parameters
Scaling weighing
checklists
Questionnaire
checklists
It is similar to scaling checklist, with additional information for the subjective evaluation of each parameter with respect to all the other parameters
These are composed of a series of questions that highlight potentially relevant issues

## Slide 11
A matrix is a grid like table that is used to identify the interaction between project activities, which are displayed along one axis, and environmental characteristics, which are displayed along the other axis.
The Leopold matrix is the best known matrix methodology available for predicting the impact of a project on the environment. The method uses a matrix with 100 specified actions and 88 environmental items (LEOPOLD et al. 1971)
These are basically generalized checklists.
Matrices

## Slide 13: Overlays and geographic information system (GIS)
Overlays can be used to map impacts spatially and display them pictorially.
The original overlay technique, popularized by McHarg, is an environmental suitability analysis in which data on topographic features, ecological values and resource constraints are mapped onto individual transparencies and then aggregated into a composite representation of potential impacts.

## Slide 14
Advantages
This approach is useful for comparing site and planning alternatives,
For routing linear developments to avoid environmentally sensitive areas and for landscape and habitat zoning at the regional level.
Disadvantages
Lack of precision in differentiating the likelihood and magnitude of impacts and relating them to project actions.
Overlay process can become cumbersome in its original form.

## Slide 15
A modern version of overlay method is the computer based geographical information system (GIS).
In simple terms, a GIS stores, retrieves, manipulates and displays environmental data in spatial format.
A set of map or overlays of a given area provide different types of information and scales of resolution.
The use of GIS for EIA purposes is not as wide spread as commonly imagined.
Drawbacks:
lack of appropriate data &
expense of creating a useful system
However, the potential application of GIS to EIA is widely acknowledged and its use is expected to increase in future, particularly to address Cumulative Effects.

## Slide 16: Networks
Networks illustrate cause effect relationship of project activities and environmental characteristics. They are therefore, particularly useful in identifying and depicting secondary impacts (indirect and cumulative etc.).
Simplified networks, used in conjunction with other methods, help to ensure that important second order impacts are not omitted from the investigation.
More detailed networks are visually complicated, time consuming and difficult to produce unless a computer program is used for the task.
However, they can be useful aid for establishing “impact hypothesis” and other structured science based approaches to EIA.
Cause Effect
Relationship

## Slide 17: Expert system
Expert or knowledge based systems are used to assist diagnosis, problem solving and decision making.
A number of such computerized systems have been developed for use in EIA, primarily at the early stages of the process.
The user has to answer a series of questions that have been systematically developed to identify impacts and determine their “mitigability” and significance.
Like GIS system, expert systems are an information intensive, high investment method of analysis, As such, they are limited in their current use and application, especially by many developing countries.
Based on the answer given to each question, the expert system moves to the next appropriate question.
Notes: For example, screening and scoping procedures have been automated using a number of rules and a data system, which encodes expert knowledge and judgement.
However, they also have the potential to be a powerful aid to systematic EIA in the future, not least because they can provide an efficient means of impact identification.
Experts systems also can be updated by building in experience gained over time.

## Slide 18
Main advantages and disadvantages of impact identification methods |  | 
Method | Advantages | Disadvantages
Checklists | easy to understand and use good for site selection and priority setting simple ranking and weighting | do not distinguish between direct and indirect impacts do not link action and impact the process of incorporating values can be controversial
Matrices | link action to impact good method for displaying EIA results | difficult to distinguish direct and indirect impacts have potential for double-counting of impacts
Networks | link action to impact useful in simplified form for checking for second order impacts handles direct and indirect impacts | can become very complex if used beyond simplified version
Overlays | easy to understand focus and display spatial impacts good siting tool | can be cumbersome poorly suited to address impact duration or probability
GIS and computer expert systems | excellent for impact identification and spatial analysis good for ‘experimenting’ | heavy reliance on knowledge and data often complex and expensive

## Slide 19
No single impact identification methodology is suited to use on all occasions; nor is it necessary to use only one method at a time. Combining the useful aspects of two different techniques may be the best approach to take.
EIA checklists, matrices and networks can have added value when applied by experts in an interactive process.
Note, also that some of the methods perform other functions that may be useful to the EIA team (e.g. the Battelle checklist can be used to determine significance).

## Slide 20
The choice of methodology can depend upon a number of factors including:
No single impact identification methodology is suited to use on all occasions; nor is it necessary to use only one method at a time. Combining the useful aspects of two different techniques may be the best approach to take.
Selection of Tool/Technique
6) The resources available- cost, information, time, personnel
4) The availability of the impact identification methods
1) The type and size of the proposal
2) The type of alternatives being considered
5) The experience of the EIA team
&
3) The nature of the likely impacts

## Slide 21: Impact Analysis/Prediction
Once all the important impacts have been identified, their potential size and characteristics can be predicted.
Impact prediction and forecasting is a technical exercise.
It utilizes physical, biological, socio-economic and cultural data to estimate likely characteristics and parameters of impacts (e.g. magnitude, spatial occurrences etc.)

## Slide 22
Characteristics of Environmental Impacts
nature (positive, negative, direct, indirect, cumulative)
  magnitude (severe, moderate, low)
extent/location (area/volume covered, distribution)
  timing (during construction, operation, decommissioning, immediate, delayed, rate of change)
  duration (short term, long term, intermittent, continuous)
  reversibility/irreversibility
  likelihood (probability, uncertainty or confidence in the prediction) and
  significance (local, regional, global)
Notes: The characteristics of environmental impacts vary. Typical parameters to be taken into account in impact prediction and decision-making include:

## Slide 23: Nature
The most obvious impacts are those that are directly related to the proposal, and can be connected (in space and time) to the action that caused them.
Typical examples of direct impacts are:
  destruction of habitat caused by forest clearance;
  relocation of households caused by reservoir impoundment;
  increased air particulate emissions caused by operation of a new power station,
  etc.

## Slide 24: Indirect or Secondary Impacts
These are changes that are usually less obvious, occurring later in time or further away from the impact source.
Examples of these types of impacts are:
  the spread of malaria as a result of drainage schemes that increase standing water and thereby create new vector habitat;
  bio-accumulation and bio-magnification of contaminants in the food chain through take up of agricultural pesticides; and
  anxiety, stress and community disruption associated with increased traffic volumes and noise caused by road development.

## Slide 25: Cumulative effects
Typically, result from the incremental impact of an action when combined with impacts from projects and actions that have been undertaken recently or will be carried out in the near or foreseeable future.
These impacts may be individually minor but collectively significant because of their spatial concentration or frequency in time.
Cumulative effects can accumulate either incrementally (or additively) or interactively (synergistically), such that the overall effect is larger than the sum of the parts.

## Slide 26
Magnitude
Estimating the magnitude of the impact is of primary importance. Typically, it is expressed in terms of relative severity, such as major, moderate or low. Severity, as opposed to size, also takes account of other aspects of impact magnitude, notably whether or not an impact is reversible and the likely rate of recovery.
Extent/Location
The spatial extent or zone of impact influence can be predicted for site-specific versus regional occurrences. Depending on the type of impact, the variation in extent/location will need to be estimated;
for example: alterations to range or pattern of species or dispersion of air and water pollution plumes.

## Slide 27
Timing
Impacts arising from all of the stages of the life cycle of the project should be considered (i.e. during construction, operation and decommissioning). Some impacts will occur immediately, while others may be delayed, sometimes by many years. These impact characteristics should be noted in the EIA report.
Significance
The evaluation of significance at this stage of EIA will depend on the characteristics of the predicted impact and its potential importance for decision-making. Significance is usually attributed in terms of an existing standard or criteria of permissible change, for example as specified in a standard, policy objective or plan.

## Slide 28: Duration
Some impacts may be short-term, such as the noise arising from the operation of equipment during construction. Others may be long-term, such as the inundation of land during the building of a reservoir.
Certain impacts such as blasting may be intermittent, whereas others, such as electromagnetic fields caused by power lines, may be continuous.
Impact magnitude and duration classifications can be cross-referenced; for example, major but short term (less than one year), low but persistent (more than 20 years).

## Slide 29: Impact Characteristics Summary Table
Impact Characteristics | Impact Type |  | 
 | Air quality | Health | Etc.
Nature |  |  | 
Magnitude |  |  | 
Extent/location |  |  | 
Timing |  |  | 
Duration |  |  | 
Reversibility |  |  | 
Likelihood (risk) |  |  | 
Significance |  |  | 

## Slide 30: Impact Prediction Methodologies
Several techniques can be used in predicting the impacts. The choices should be appropriate to the circumstances. These can be based on:
Professional judgment with adequate reasoning and supporting data. This technique requires high professional experience
Experiments or tests. These can be expensive
Past experience
Numerical calculations & mathematical models. These can require a lot of data and competency in mathematical modelling without which hidden errors can arise
Physical or visual analysis. Detailed description is needed to present the impact.
Geographical information systems
Risk assessment and
Economic evaluation of environmental impacts

## Slide 31: Methods for Predicting the Characteristics of Impacts
Predicting the Characteristics of Impacts
‘Best estimate’ professional judgement
Experiments and physical models
Case studies as analogues or points of reference
Quantitative mathematical models

## Slide 32: Types of Uncertainties in Impact Prediction
Scientific uncertainty: limited understanding of the ecosystem or community affected
Data uncertainty: incomplete information or insufficient methodology
Policy uncertainty: unclear or disrupted objectives or standards
Approaches to Address Uncertainties in Impact Prediction
“Best” and “worst” case prediction to illustrate the spread of uncertainty
Attaching confidence limits to impact predictions; and
“Sensitivity analysis to determine the effect of small changes in impact magnitude

## Slide 33: Evaluation of impact significance
Impact characteristic (magnitude)
M
Impact importance (value)
I
Impact significance
S
X
M X I = S

## Slide 34: Key Elements for Assessing Impact Significance
Environmental standards, guidelines & objectives
Level of public concern
Resource loss/ecological damage
Negative social impacts
Foreclosure of land and resource use options
Scientific and professional evidence concerning:
Test of Significance by Asking Three Questions
Are there residual environmental impacts?
If yes, are these likely to be significant or not?
If yes, are these significant effects likely to occur?

## Slide 35: Impacts are likely to be significant if they:
Are expensive over space or time
Are intensive in concentration or in relation to assimilative capacity
Exceed environmental standards or thresholds
Do not comply with environmental policies/ land use plans
Affect ecological sensitive areas and heritage resources
Affect community lifestyle, traditional land use and values

## Slide 36: Thank You!!